Power A Free Life

CONTENTS

ECOFLOW STORY

OUR TECHNOLOGY

RIVER 600

RIVER 600 MAX

RIVER 600 PRO

EF DELTA

SOLAR PANEL

ACCESSORIES

FOLLOW OUR STORY

01

06

09

11

12

16

21

24

25

ECOFLOW STORY

Our mission is to empower both individuals and communities

through portable, clean, reliable power a lasting impact by

replacing the traditional gas generator and reinventing the way

the world accesses energy.

Now, EcoFlow leverages their rich knowledge and experience

to build products that are thoughtful in design, smart, and

powerful. We strive to reinvent the way people everywhere

access power.

EcoFlow’s product lines equip our customers with a substantial

amount of clean, quiet, and renewable power for work,

adventures, and home backup power.

1

LITHIUM-ION BATTERY

GENERATOR

NO FUEL, NOISE, OR FUMES

No gasoline, toxic fumes, or noise/vibration during operation. The

EcoFlow Power Station is safe to use indoors.

NO MAINTENANCE

Easy to use, keep it plugged into a wall outlet or solar panel.

NO LOST POWER

Power is stored and consumed as needed, maximizing efficiency.

LOW COST

Costs 30% less than regular gasoline-powered inverter generators over its

lifetime.

2

OUTDOORS

Enjoy your next adventure with full

power.

· Van Life

· Camping

· Festivals

· Tailgating

3

EMERGENCY

Always be prepared for the

unpredictable.

· Home Backup

· Disaster Relief

· Medical Devices

4

PROFESSIONAL

Get the job wrapped up with

uninterrupted power.

· DIY

· Film/Photography

· Event Production

5

OUR TECHNOLOGY

Patented X-Stream Technology

From 0 to 80% Within 1 Hour

For the past three years, we've dedicated

our time and energy to create the X-Stream

Recharge Technology. This technology

provides the fastest recharge rate on the

market, recharging 5x times faster than

counterparts. This allows EcoFlow products

to be fully recharged within two hours using

any regular wall outlet.

Battery Management

System

We’ve developed our own prominent

Battery Management System to extend

the performance, lifecycle, and shelf-life

of EcoFlow products. This regulates all

the batteries inside the unit and manages

the health and efficiency of each one,

individually using AI algorithms.

Patented BMS System

ECOFLOW APP

In this wireless world, remote control use is the standard. Now you can pair EcoFlow

products over Wi-Fi with the EcoFlow mobile app. It does everything straight from

the palm of your hand.

Download on the

App Store

Download for

Android

OUR PRODUCTS

Our product lines range from the powerful DELTA to the

flexible modular RIVER 600 series, which can fulfill your

power demand in many different scenarios.

Portable Power Station

AC Output

600

(Surge 1200W)

NEW

RIVER 600

RIVER 600, with its unprecedented modular

design, elevates the portable power station to a

whole new level of performance and efficiency. You

can customize your system to exactly what suits

you. Designed with a transformative 600W inverter

with X-Boost technology, RIVER 600 pushes the

boundaries of what a portable power station can

do.

OUTPUTS:

AC Output (x3/x2): 600W (Surge 1200W)

USB-A Output (x2): 12W per port, 5V DC, 2.4A

USB-A Fast Charge (x1): 28W, 5V DC,

9V DC,12V DC, 2.4A Max

USB-C Output (x1): 100W, 5V DC, 9V

DC,12V DC, 15V DC, 20V DC, 5A Max

Car Power Output (x1): 136W, 13.6V DC, 10A Max

DC5521 Output (x2): 13.6V DC, 3A Max (per port)

INPUTS:

AC Charge Input Power, X-STREAM: 250W Max

AC Charge Input Voltage: 100-120Vac (50Hz/60Hz)

(Int’l Version 220-240V)

Solar Charge Input: 200W 10-25V DC 12A Max

Car Charge Input: 12V/24V DC 10A Max

BATTERY:

Cell Chemistry: Lithium-ion

Cycle Life: 500+ Cycles (80%)

Discharge Temp: -4 to 140°F +/-5°F (-20 to 60°C +/-3°C)

Charge Temp: 32 to 113°F +/-5°F (0 to 45°C +/-3°C)

GENERAL SPECS:

Capacity: 288Wh

Weight: 11 lbs (5kg)

Dimensions: 11.3 x 7.3 x 7.7in (28.8 x 18.5 x 19.4cm)

10

NEW

RIVER 600

By attaching the RIVER 600 Extra Battery, the

RIVER 600 Max doubles its capacity, but still

retains its portability and flexibility. You can

even set it to ambient light for date night.

OUTPUTS:

AC Output (x3/x2): 600W (Surge 1200W)

USB-A Output (x2): 12W per port, 5V DC, 2.4A

USB-A Fast Charge (x1): 28W, 5V DC, 9V DC,12V

DC, 2.4A Max

USB-C Output (x1): 100W, 5V DC, 9V DC,12V DC,

15V DC, 20V DC, 5A Max

Car Power Output (x1): 136W, 13.6V DC, 10A Max

DC5521 Output (x2): 13.6V DC, 3A Max (per port)

INPUTS:

AC Charge Input Power, X-STREAM: 500W Max

AC Charge Input Voltage: 100-120Vac (50Hz/60Hz)

(Int’l Version 220-240V)

Solar Charge Input: 200W 10-25V DC 12A Max

Car Charge Input: 12V/24V DC 10A Max

BATTERY:

Cell Chemistry: Lithium-ion

Cycle Life: 500+ Cycles (80%)

Discharge Temp: -4 to 140°F +/-5°F (-20 to 60°C +/-3°C)

Charge Temp: 32 to 113°F +/-5°F (0 to 45°C +/-3°C)

GENERAL:

Capacity: 576Wh

Weight: 17 lbs (7.7kg)

Dimensions: 11.3 x 7.3 x 9.96in (28.8 x 18.5 x 25.3cm)

11

NEW

RIVER 600

The RIVER 600 PRO is designed for users seeking

a power solution with a longer runtime. With

the 720Wh lithium-ion battery pack and built-in

EcoFlow BMS, the RIVER 600 PRO enjoys 500+

lifecycles and can easily expand to a capacity of

1440Wh by connecting the RIVER 600 PRO Extra

Battery with just a simple cable.

OUTPUTS:

AC Output (x3/x2): 600W (Surge 1200W)

USB-A Output (x2): 12W per port, 5V DC, 2.4A

USB-A Fast Charge (x1): 28W, 5V DC, 9V DC,12V

DC, 2.4A Max

USB-C Output (x1): 100W, 5V DC, 9V DC,12V DC,

15V DC, 20V DC, 5A Max

Car Power Output (x1): 136W, 13.6V DC, 10A Max

DC5521 Output (x2): 13.6V DC, 3A Max (per port)

INPUTS:

AC Charge Input Power, X-STREAM: 660W Max

AC Charge Input Voltage: 100-120Vac (50Hz/60Hz)

(Int’l Version 220-240V)

Solar Charge Input: 200W 10-25V DC 12A Max

Car Charge Input: 12V/24V DC 10A Max

BATTERY:

Cell Chemistry: Lithium-ion

Cycle Life: 500+ Cycles (80%)

Discharge Temp: -4 to 140°F +/-5°F (-20 to 60°C +/-3°C)

Charge Temp: 32 to 113°F +/-5°F (0 to 45°C +/-3°C)

GENERAL:

Capacity: 720Wh

Weight: 16 lbs (7.2kg)

Dimensions: 11.3 x 7.3 x 9.96in (28.8 x 18.5 x 25.3cm)

12

NEW

RIVER 600 PRO

EXTRA BATTERY

The RIVER 600 PRO Extra Battery, with 500+

lifecycles, can double the capacity of the

entire system when connected to the RIVER

600 PRO.

OUTPUTS:

Expansion Power Port: 600W Max

INPUTS:

Expansion Power Port: 660W Max

BATTERY:

Cell Chemistry: Lithium-ion

Cycle Life: 500+ Cycles (80%)

Discharge Temp: -4 to 140°F +/-5°F (-20 to 60°C +/-3°C)

Charge Temp: 32 to 113°F +/-5°F (0 to 45°C +/-3°C)

GENERAL:

Capacity: 720Wh

Weight: 15.4 lbs (7kg)

Dimensions: 11.3 x 32.4 x 6.5in (28.8 x 21.7 x 16.5cm)

13

1. LCD Display

Display various conditions of the product.

2. LED Light Control Button

There are three types of LED light: low light,

strong light, and SOS rescue signal flash.

3. IOT Reset Button

Used to reset the Wi-Fi.

4. USB-C 100w Output Port

The 100W USB-C port can support output power

up to 100w, you can even charge a laptop.

5. USB-A Output Ports

Charge a wide spectrum of devices including

iPhone, tablet, GoPro, speakers, or anything else

that can be charged through a USB Port.

6. Fast Charge USB-A Output Port

Fast-charge enabled devices can be charged at

a maximum output of 28W.

7. Power Button

Press and hold the button to turn RIVER 600 on

or off.

8. DC Output Port (Car Outlet, 2 Dc

5521 Output Ports) DC Output Indicator

The DC 12V port is used to charge appliances

like mini PC, projector, Wi-Fi Router or 12V Light.

The car cigarette output port can be used for a

car fridge.

1

9. Ventilation Fan

The fan prevents RIVER 600 from overheating.

10. 3*AC Output Sockets (100-120v)

2*AC Output Sockets (220-240v)

The powerful AC output sockets can support

your daily home appliances, and with the X-boost

feature on, it can even be used for a kettle.

11. AC Power Button

The AC power button controls the AC output of

the RIVER 600.

12. Expansion Power Port

This port is used to connect the RIVER 600 PRO

Extra Battery to provide increased capacity.

13. X-Stream Charging Input Port

The fastest X-stream charging input port in the

industry, AC recharge 0-80% within one hour.

14. Overload Protection Switch

When the input current continuously exceeds

10A during a charge, the AC charging port will

trigger the overload protection.

15. Power Earth Screw

The power earth screw provides an option to get

your RIVER 600 grounded using a grounding cable.

16. Solar Charge/Car Charge Input Port

Support a maximum of two 110W solar panels

to be connected in parallel. It also supports a

12V/24V car charge up to 10A.

2

4

5    6

10

9

13      14      15

11

16

7

12

14

RIVER 600 SERIES

COMPARISONS

RIVER 600     RIVER 600 MAX   RIVER 600 PRO   RIVER 600 PRO

with Extra Battery

15

Lithium-ion Battery Generator

AC Output         Capacity

1800  1260

(Surge 3300W)             Wh

EF DELTA

EF DELTA, the lithium-ion battery generator

with high power output, large capacity, and

groundbreaking recharging technology. Has

the same power as a traditional gasoline

generator, but without noise, emissions, and

high maintenance fees.

OUTPUTS:

AC Output (x6)/AC Output (x4): 1800W (Surge

3300W) total, 120Vac (60Hz)/230Vac (50Hz)

USB-A Output (x2): 12W 5V DC, 2.4A Max, per port

USB-A Fast Charge (x2) : 28W 5V DC, 9V DC, 12V

DC, 2.4A Max, per port

USB-C Output (x2): 60W 5V DC, 9V DC, 15V DC,

20V DC, 3A Max, per port

Car Power Output (x1): 108.8W, 13.6V DC, 8A Max

INPUTS:

AC Charge Input Voltage: 100-120Vac (50Hz/60Hz)

ONLY! (International Version 220-240Vac ONLY!)

AC Charge Input Power: 1200W Max

Solar Charge Input: 400W 10-65V DC 10A Max

Car Charger: 12V/24V DC 10A Max

BATTERY:

Cell Chemistry: Lithium-ion

Cycle Life: 800+ Cycles (60%)

Discharge Temp: -4-140°F +/-5°F (-20-60°C +/-3°C)

Charge Temp: 32-113°F +/-5°F (0-45°C +/-3°C)

GENERAL:

Capacity: 1260Wh

Weight: 30.9lbs (14kg)

Dimensions: 15.7 x 8.3 x 10.6in (40 x 21 x 27cm)

17

1

7 8

9

10

2

3

3

4                                                        11

5

6

1. LCD Display

Display the various conditions of the product.

2. USB-A Output Ports

Charge a wide spectrum of devices including

iPhone, tablet, GoPro, speakers, or anything

else that can be charged through a USB port.

3. Fast Charge Usb-A Output Ports

Charge devices at double the speed.

4. USB-C Output Ports

Charge your laptop, mobile phone etc.

5. DC On/Off Switch

Control the DC output.

6. Power On/Off Button

Press and hold the power button to turn the EF

DELTA on or off.

7. Solar Charge/Car Charge Input Port

Support a maximum of four 110W solar panels

to be connected. It also supports a 12V/24V car

charge up to 10A.

12

8. X-Stream AC Charge Input Port

The X-stream charging input port in the industry,

AC recharge 0-80% within one hour.

9. Overload Protection Switch

When the input current continuously exceeds 20A

during a charge, the AC charging port will trigger

the overload protection.

10. 6*AC Output Sockets (100-120v)

4*AC Output Sockets (220-240v)

Charge devices, such as laptop, electric guitar, TVs,

mini refrigerator, vacuum etc.

11. AC Power Button

The AC Power Button controls the AC output of EF

DELTA.

12. Car Outlet

Charge devices like a drone battery, car fridge or

any device using a car socket.

18

RUN TIMES

RIVER 600          RIVER 600 MAX        RIVER 600 PRO         EF DELTA

LIGHT

12 Hours

24 Hours

32 Hours

60 Hours

(10W)

14 Times         28 Times         38 Times        63 Times

PHONE

(18Wh)

2.5 Times

5 Times

7 Times

11.5 Times

LAPTOP

(99Wh)

10 Times

21 Times

27 Times

45 Times

SONY A7IV

(25Wh)

2-4 Hours

4-8 Hours

5-10 Hours

8-16 Hours

TELEVISION

(110W)

GRILL

0.4 Hours

0.8 Hours

1 Hours

0.6-1.2 Hours

(1650W)

CPAP

5-10 Hours

10-20 Hours

13-26 Hours

20-40 Hours

(40W)

REFRIGERATOR

1.5-3 Hours

3-6 Hours

4-8 Hours

6-10 Hours

(150W)

19

CHARGING TIMES

RIVER 600         RIVER 600 MAX        RIVER 600 PRO

EF DELTA

INCLUDED

POWER SUPPLY

1.6 Hours

1.6 Hours

1.6 Hours

1.6 Hours

1.6 Hours

1.6 Hours

1.6 Hours

1.6 Hours

GAS GENERATOR

3 Hours

5 Hours

6.5 Hours

10 Hours

CAR CHARGER

SOLAR PANEL

(110W)

1.6-3 Hours

（110W*4）

SOLAR PANEL

7 Hours

14 Hours

19 Hours

(60W)

SOLAR CHARGING

RECOMMENDATIONS

RIVER 600          RIVER 600 MAX       RIVER 600 PRO

EF DELTA

LITE USE

20% DAILY

60 WATTS        60 WATTS        60 WATTS       110 WATTS

MEDIUM USE

50% DAILY

110 WATTS

110 WATTS        110 WATTS       330 WATTS

HEAVY USE

100% DAILY

220 WATTS       220 WATTS       220 WATTS      440 WATTS

20

SOLAR PANELS

Whetheryou're recharging aa portablerefueling portable power

monocrystallineportable panel monocrystalline solar panels are

rugged,Providing power in an eco-friendly manner.

Harness the sun to power your life.

21

60W SOLAR PANEL

The 60W solar panel is lightweight for easy

transporting and convenient to operate. Plug in

and power whenever and wherever.

60W SOLAR PANEL:

Rated Power: 60W (+/-5W)

Open Circuit Voltage: 21.6V (Vmp 18.2V)

Short Circuit Current: 3.5A (Imp 3.3A)

Efficiency: 21-22%

Cell Type: Monocrystalline silicon

OUTPUT PORTS:

MC4 Solar Port to XT60: 80V (Max), up to 10A (Max)

GENERAL:

Weight: 7.7 lbs (3.5KG) Solar Panel 4.4lbs (2.0KG)

Waterproof IP Ratings: IP67

Unfolded Dimensions: 21*32.1*0.8in (53.7*81.5*2cm)

Folded Dimensions: 21*16.5*0.8in (53.7*42*2cm)

22

110W SOLAR PANEL:

Rated Power: 110W(+/-5W)

Open Circuit Voltage: 21.7V(Vmp 18.5V)

Short Circuit Current: 6.3A(Imp 6.0A)

Efficiency: 21-22%

Cell Type: Monocrystalline silicon

OUTPUT PORTS:

MC4 Solar Port to XT60: 80V(max), up to 10A (max)

GENERAL:

Weight: 13.2 lbs(6KG) Solar Panel 8.8 lbs(4.0KG)

Waterproof IP Ratings: IP67

Unfolded Dimension: 20.2*62.5*0.8in (51.4*158*2.0cm)

Folded Dimension: 20.2*16.5*0.8in (51.4*42*2.0cm)

110W SOLAR PANEL

Live off the grid with your 110W solar panels.

Created from the most efficient monocrystalline

silicon cells, recharge the EF DELTA or RIVER,

and keep your equipment running without

interruption.

23

ACCESSORIES

24

Follow Our Story

Follow Us:

Facebook:

@EcoFlowTech

Contact Us:

Instagram:

@EcoFlowTech

Twitter:

@EcoFlowTech

Support

Wholesale              Marketing

support@ecoflow.com

sales@ecoflow.com

(North America & Others)

sales-EU@ecoflow.com

(Europe&Australia)

marketing@ecoflow.com

25

POWER A FREE LIFE

www.ecoflow.com

# Text boxes

3                       8

| Capacity | 288Wh | 576Wh | 720Wh | 1440Wh |
| --- | --- | --- | --- | --- |
| Battery Chemistry | Lithium-ion | Lithium-ion | Lithium-ion | Lithium-ion |
| Shelf Life | 1 Year | 1 Year | 1 Year | 1 Year |
| Cycle Life | 500+(80%) | 500+(80%) | 500+(80%) | 500+(80%) |
| AC Output | 600W (Surge 1200W) | 600W (Surge 1200W) | 600W (Surge 1200W) | 600W (Surge 1200W) |
| AC Ports | 3 | 3 | 3 | 3 |
| Type-C PD Ports | 100W (Support Macbook Pro) | 100W (Support Macbook Pro) | 100W (Support Macbook Pro) | 100W (Support Macbook Pro) |
| Total Ports | 10 | 10 | 11 | 11 |
| Wall Charging | 250W Max | 550W Max | 660W Max | 660W Max |
| Wall Charging Time | 1.6 Hours | 1.6 Hours | 1.6 Hours | 3 Hours |
| Universal Solar Charging (MC4) |  |  |  |  |
| Solar Panel Charging | 200W (110W*2) | 200W (110W*2) | 200W (110W*2) | 200W (110W*2) |
| Solar Panel Charging Time | *1.6-3 Hours (110W*2) | *3-6 Hours (110W*2) | *4-8 Hours (110W*2) | *8-16 Hours (110W*2) |
| APP |  |  |  |  |
| Weight | 11 lbs | 17 lbs | 16 lbs | 32 lbs |

（110W*2）        3-6 Hours

（110W*2）       4.5-9 Hours

（110W*2）       4-8 Hours

When               phone   power station, our

station, our   solarline of efficient, reliable, and easy

to use. reliable, and easy to use.

| PRODUCT | NAME | DESCRIPTION |
| --- | --- | --- |
|  | Solar MC 4 Parallel Connection Cable | Solar MC 4 parallel connection cable can be used to connect 4 or 6 solar panels to charge your EcoFlow product. |
|  | Suction Cups for Solar Panel | Suction Cups (8pcs per package): Easy to attach to glass, the car roof, and other smooth surfaces. Best method of securing solar panels. |
|  | MC4 to XT60 Solar Panel Charging Cable | With this EcoFlow MC4 to XT60 cable, a solar panel with a standard MC4 output can be connected to the power station. |
|  | AC Charging Cable | Connect to a wall outlet to recharge your power station. |
|  | Car Charging Cable | Connect your car to recharge your power station. |
|  | DC5521-DC5525 Cable | Connect appliances with DC type port. e.g, computer monitor, mini-computer, LED light, Wi-Fi router. |
|  | Expansion Power Cable | Connect your RIVER 600 PRO with a RIVER 600 PRO extra battery. |